## Slide 1
DIGITAL LOGIC • MINI PROJECT
4-BIT UNIVERSAL SHIFT REGISTER
Design • Logic Gates • Simulation
Q0
Q1
Q2
Q3
Presented by: _K.GOUTHAM_ Roll No: _2620090025_

## Slide 2
01
What is a Shift Register
◆
A shift register stores binary data using flip-flops.
◆
A 4-bit register can store four bits: Q3 Q2 Q1 Q0.
◆
On each clock pulse, the stored data can move or be replaced.
◆
It is widely used in digital systems for storage and data transfer.

## Slide 3
02
Why “Universal”?
◆
One circuit can perform four useful operations.
◆
Hold the current data.
◆
Shift data right or shift data left.
◆
Load four new bits simultaneously using parallel inputs.

## Slide 4
03
The Four Modes
00 HOLD
01 SHIFT RIGHT
10 SHIFT LEFT
11 PARALLEL LOAD
S1 S0

## Slide 5
04
Inside the 4-Bit Register
◆
Four D flip-flops form the storage section.
◆
Each flip-flop stores one binary bit.
◆
All flip-flops share the same clock.
◆
Logic gates choose the next value for each D input.

## Slide 6
05
Logic-Gate Idea
◆
AND gates enable the required data path.
◆
OR gates combine the selected paths.
◆
NOT gates provide the required complementary control signals.
◆
Together, the gates behave like a 4-to-1 data selector for each flip-flop.

## Slide 7
06
Control Table
S1 | S0 | Operation | Action
0 | 0 | Hold | No change
0 | 1 | Shift Right | Bits move to the right
1 | 0 | Shift Left | Bits move to the left
1 | 1 | Parallel Load | Loads 4-bit data at once

## Slide 8
07
Simulation: A Simple Run
◆
Start with register = 1011.
◆
Select SHIFT RIGHT and apply a clock pulse → 0101*.
◆
Select PARALLEL LOAD with 1100 → register becomes 1100.
◆
Select HOLD → register stays 1100.
◆
*Example assumes serial input 0.

## Slide 9
08
How to Verify the Design
◆
1. Set S1 and S0.
◆
2. Apply the required parallel or serial input.
◆
3. Give one clock pulse.
◆
4. Observe Q3, Q2, Q1 and Q0.
◆
5. Compare the result with the selected mode.

## Slide 10
09
Real-World Applications
◆
Serial-to-parallel and parallel-to-serial data transfer.
◆
Temporary data storage in digital circuits.
◆
Data movement inside processors and controllers.
◆
Communication and signal-processing systems.

## Slide 11
10
Key Takeaways
◆
4 flip-flops = 4 bits of storage.
◆
Two control lines select four operating modes.
◆
Logic gates decide which data reaches each flip-flop.
◆
The clock controls when the selected data is stored.
◆
The same hardware can perform several data-transfer operations.

## Slide 12
11
Conclusion
STORE
SHIFT
LOAD
CONTROL
A compact circuit with multiple capabilities — controlled by just two mode-select inputs and a clock.

## Slide 13
THANK YOU